PRESS RELEASE	Symbol: GRIN

October 24, 2007	CNQ Stock Exchange www.cnq.ca

URL www.goldreef.ca

## GOLD REEF INTERNATIONAL RELEASES PHASE 1 DRILL RESULTS FROM THE GOLDEN TRAIL PROJECT, ELKO COUNTY, NEVADA

Toronto, Canada, October 24, 2007 - Gold Reef International, Inc. (CNQ: GRIN) has received analytical results for four reverse circulation drill holes totaling 8,100 feet on the Golden Trail gold prospect in Elko County, Nevada.  Gold Reef intends to drill a total of 18 angle holes and 4 deep vertical holes in a two-phase program to test both shallow high-angle northwest trending structurally associated mineralization and also deeper igneous intrusive associated targets.

The initial phase of four vertical 2,000 foot reverse circulation holes tested the northeast and southwest margins of the northwest-trending strong gravity high centered on  mineralized northwest-striking high angle structures. The strongly decalcified and hydrothermally altered Paleozoic sedimentary complex of limestone, siltstone, sandstone, chert and quartzite that hosts the mineralization is anomalous in gold and pathfinder elements including antimony, arsenic, copper, mercury, molybdenum, silver and zinc.  All four drill holes encountered a 560 to 640 foot section of thermally metamorphosed and jasperoidal limestone, siltstones and calcareous shale which overlie highly carbonaceous and calcareous shale, siltstone, chert, limestone, and dolomite. Phlogopite-dolomite hornfels was identified by X-ray diffraction analyses (XRD) deep in drill hole GT17. None of the vertical holes intersected the high-angle structural zones, which will be the focus of the second phase of drilling in the spring of 2008.  Samples along the high-angle northwest-striking structures include the previously reported 28.1 grams per tonne (gpt) gold and 35.7 gpt Ag rock chip sample and four additional samples of 1.004 gpt, 2.0 gpt, 2.91 gpt and 9.04 gpt.

Gold Reef has selected 90 specific samples of the drill hole cuttings for further thin section and X-ray diffraction tests to determine mineralogy and investigate the possibility

of vectoring to the prospective intrusive, which may be responsible for the wide dispersion of gold and pathfinder elements in surface samples.

Significant drill hole results include a 20 foot intercept in a silicified shale in GT12 from 655 to 675 feet which assayed an average of 0.236 gpt Au. In addition thick sections of significantly anomalous zinc were encountered in a hornfels section of each drill hole as shown in the table below.

| Zinc Intercepts |
| --- |
| Hole | From | To | Thickness | % Zn |  |
| GT8 | 1280 | 1490 | 210 | 0.0382 |  |
|  | 1865 | 1930 | 65 | 0.0791 | Incl. 1875-1890 @ 0.12 % |
| GT9 | 1300 | 1550 | 250 | 0.0450 | Incl. 1480-1500 @ 0.14 % |
|  | 1810 | 2010 | 200 | 0.0716 |  |
| GT12 | 1200 | 1495 | 295 | 0.0487 |  |
|  | 1720 | 2010 | 290 | 0.0704 | Incl. 1805-1815 @ 0.36% |
| GT17 | 1225 | 1490 | 265 | 0.0460 |  |
|  | 1655 | 1720 | 65 | 0.1197 | Incl. 1670-1680 @ 0.59 % |
|  | 1745 | 2035 | 280 | 0.0797 | Incl. 1810-1880 @ 0.11% |

Each of the zones shown in the table had significantly elevated vanadium including a 160 foot interval from 1790 to 1950 feet in GT17, which averaged 589 ppm V. Molybdenum was also highly anomalous in each hole consistent with the zones with anomalous zinc content.

Gold Reef geologists will continue to analyze the geochemical data in conjunction with the thin section study to vector into future drilling targets.  The following table summarizes data from the four holes compared to surface sampling results. Although additional study is required it appears that gold is significantly more anomalous in GT 8 and GT9 than in GT 12 and GT17, whereas the base metal anomalies stay relatively the same.

| # Anomalous | Au | Ag | As | Hg | Pb | Sb | Zn | Mo | Cu |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| GT8 | 331 | 329 | 96 | 65 | 71 | 346 | 362 | 286 | 361 |
| GT9 | 317 | 344 | 85 | 66 | 65 | 357 | 357 | 238 | 354 |
| GT12 | 192 | 338 | 125 | 51 | 49 | 359 | 391 | 281 | 343 |
| GT17 | 140 | 402 | 180 | 109 | 72 | 404 | 405 | 334 | 366 |
| % Anomalous |  |  |  |  |  |  |  |  |  |
| GT8 | 87 | 86 | 25 | 17 | 19 | 91 | 95 | 75 | 95 |
| GT9 | 79 | 86 | 21 | 16 | 16 | 89 | 89 | 59 | 88 |
| GT12 | 48 | 84 | 31 | 13 | 12 | 89 | 97 | 70 | 85 |
| GT17 | 33 | 93 | 42 | 25 | 17 | 94 | 94 | 78 | 85 |
| Surface samples | 35 | 67 | 30 | 12 | 56 | 87 | 83 | 46 | 38 |

All of the drill hole data has been incorporated into Gold Reef’s Metal Miners Plus© data management/interpretative system to prioritize drilling targets and enable instant comprehensive data retrieval.

About Gold Reef International, Inc.:

Gold Reef International, Inc. is a well-financed exploration company with a growing portfolio of prospective precious metals properties in Nevada.  Gold Reef has five claim blocks totaling 11,867 acres, which from surface sampling programs contain significantly anomalous gold and pathfinder elements. In addition to NI 43-101 compliant geologic reports on the Golden Trail and Texas Canyon Prospects in Elko County, Gold Reef is currently conducting detailed mapping, sampling and geophysics on the Rimrock Project in Lander County, which is subject to a lease agreement with Newmont and the Golden Badger gold-zinc-moly project in Elko County.

Dr. Criss Capps, Gold Reef’s Vice President of Exploration, is the “qualified person” within the meaning of NI 43-101 and has reviewed the technical contents of this press release on behalf of the Company.

For further information, please contact Lou Kost, Jr., at Gold Reef International, Inc., (210) 821-6511 or Andrew Kaplan, at Barry Kaplan Associates, (732) 747-0702.